## Slide 1: Inverse problems project
Today:
Placeholder for what we want to discuss.

## Slide 2: Problem overview
🏥 Understand differences in CT image reconstruction: Compare how different reconstruction algorithms (e.g. iDose vs IMR vs FBP) affect the final medical images from the same sinogram data. Investigate the effect of noise on both methods.
🔁 Investigate cross-hospital image compatibility: Develop methods to harmonise images reconstructed by different algorithms so that they can be meaningfully shared and interpreted across hospitals.
🔎 Investigate reversibility and transformation: Explore whether images from one reconstruction method (e.g. iDose) can be transformed to resemble another (e.g. IMR).

## Slide 3: Sinogram -> image
Filter Back projection (FBP)  not stable because of noise.
Iteratieve method:
min_ x L(x) = min _ x 1/2 || Ax –y || ^2 + R(x)
d L(x)/ dx = A^(*T) (A x – y) + R’(x)
A: radon transfrom
x: sinogram
y: sinogram
Q: Is A^*t gelijk aan iradon zonder filter?

## Slide 4: Initial results using FBP
FBP:
# theta = 180
Filter: ‘ramp’

## Slide 5: Initial results using FBP
FBP:
# theta = 100
Filter: ‘ramp’
Less theta  noise hits
harder.

## Slide 6: Initial via iterative method
FBP:
# theta = 100
Filter: ‘ramp’
It = 5
No regulariser

## Slide 7: Initial with regularisor
FBP:
# theta = 100
Filter: ‘ramp’
It = 5
No regulariser
I tried Cauchy prior, TV with a proxy but it doesnot make it much better

## Slide 9: Vragen
In IMR the A has physcial prior information it is now hard to implement this in our model.
What is the expect noise? It would be log of poision noise right?